## Slide 1: CE4055 LAB:3
CODE Analysis of Firmware and PAT

## Slide 2: We will learn:
Writing firmware for AVR MCUs
UART Communication
Code analysis of SCA Firmware code
Code analysis of PAT tool (CPA)

## Slide 3: Software/Firmware used
Firmware
Written in Embedded C
  AES code
  UART controller
  AES controller
Communicates with PC
Sends binary signal to oscilloscope
Software
Written in C#
  Serial Communication
  Oscilloscope settings
  Saving waveforms to file
Communicates with both Oscilloscope and AVR board
Software
Written in JAVA
  Reads trace files
  Performs CPA
No communication with other tools or devices

## Slide 4: Firmware coding into AVR Microcontroller
Download ATMEL Studio – the perfect IDE for AVR coding
Write code in Embedded C
Burn code into MCU using AVR ISP or other programmer or simply use Arduino programmer if bootloader already present on chip

## Slide 5: Understanding the SCA Firmware code
#define BAUD 38400
#define MYUBRR F_CPU/16/BAUD-1
/* SETUP UART */
void USART_Init( unsigned int ubrr){
/*Set baud rate */
UBRR0H = (unsigned char)(ubrr>>8);
UBRR0L = (unsigned char)ubrr;
/*Enable receiver and transmitter */
UCSR0B = (1<<RXEN0)|(1<<TXEN0);
/* Set frame format: 8data, 2stop bit */
UCSR0C = (1<<USBS0)|(3<<UCSZ00);
}
//uart transmit receive functions
. void SendBytes(unsigned char *StringPtr, int length){..}
. uint8_t readByte(){..}
//
uint8_t pre[] = {0x01, 0x23, 0xAB, 0xCD};
uint8_t key[] = {0x48, 0x9D, 0xB4, 0xB3, 0xF3, 0x17, 0x29, 0x61, 0xCC, 0x2B, 0xCB, 0x4E, 0xD2, 0xE2, 0x8E, 0xB7};
void DoStuff()
{
uint8_t plaintext[16];
for(int i=0; i < 16 ; i++)
{
plaintext[i] = readByte();
}
aes128_enc_tiny_full(plaintext, key);
SendBytes(pre, 4);
SendBytes(plaintext, 16);
}
void updateKey(){
uint8_t newkey[16];
for(int i=0; i < 16 ; i++)
{
newkey[i] = readByte();
}
for(int i=0; i < 16 ; i++)
{
key[i] = newkey[i];
}
}
int main(void){
//Setup Serial
USART_Init(MYUBRR);
DDRB = 0x02; //using PB1 for trigger
PORTB = 0x00; //turning low
while(1)
{
if(readByte() == 0x01)
{
if(readByte() == 0x23)
{
if(readByte() == 0xAB)
{
if(readByte() == 0xCD)
{
DoStuff();
}
}
}
}
else
{
if(readByte() == 0x67)
{
if(readByte() == 0xAB)
{
if(readByte() == 0xCD)
{
updateKey();
}
}
}
}
_delay_ms(100);
}
}

## Slide 6: Understanding the SCA Firmware code (contd.)

## Slide 7: The Process flow diagram
While (1)
If,
Byte_1=01
Byte_2=23
Byte_3=AB
Byte_4=CD
Next 16 bytes are plaintext
dostuff()
Else If,
Byte_1=45
Byte_2=67
Byte_3=AB
Byte_4=CD
Next 16 bytes are key bytes
updateKey()
aes128_enc_tiny_full(plaintext, key)
firstround()
PORTB = 0x02
State[i] = sbox[state[i]]
PORTB = 0x00

## Slide 8: PAT

## Slide 9: Understanding the PAT Code (CPA)

## Slide 10: Lab Copy (Assignment)
To be submitted individually
Should have both lab details in the same report copy
It should contain the following parts for each lab:
  Introduction
  Proceedings of lab
  Inference
  Conclusion

## Slide 11: Project Report
To be submitted in a group
Problem statement:
  Write Correlation Power Analysis code in any language of your choice and use the collected traces to retrieve the key
  The code should be able to generate a graph of “no. of traces vs bits recovered” and “correlation coefficient vs no of traces” as shown in the graph above
  Write a brief literature survey of existing countermeasures against power analysis attacks
  Conclusion
Each code will be checked for similarities with codes of other students and copying may result to redo the project with different topic

## Slide 12: Thank you
Questions?